Objectives: Our objectives was to design a 12 Bit ISA which can solve a particular problems i. e. Simple arithmetic & logic operations, branching and loops.

Operands: Our goal is to use accumulator base ISA. For this reason we are going to take two operands. We will address these two operands as d and s.

Types of Operands: To implement arithmetic instruction we need register operands and for data transfer instruction from memory to register we need memory operands. So we need two types of operands.
- Register based.
- Memory based.

Operations: We will allocate 4 bits opcode, so the executable instructions number will be 24 or 16.

Types of operations: In our design there will be five different types of operation. The operations are:
- Arithmetic
- Logical
- Data Transfer
- Conditional Branch
- Unconditional Jump

Category	Operation	Name	Type	Opcode	Syntax	Comments
Arithmetic	Add two numbers	add	R	0000	add, / $s1,$s2	$s1 = $s1 + $s2
Arithmetic	Add number with an immediate	addi	I	0001	addi / $s1, 5	$s1 = $s1 + 5
Arithmetic	subtraction	sub	R	0010	sub / $s1, $s2	$s1 = $s1 - $s2
Logical	Shift left	sll	I	0011	sll / $s1, 2	$s1=$sp<<2
Logical	Bit –by-bit and	And	R	0100	And / $s1 , $s2	$s1=$s1 & $s2
Logical	Bit –by-bit nand	Nand	R	0101	Nand / $s1,$s2	$s1 = $s1 Nand $s2
Data transfer	Load word	lw	I	0110	lw / $s3, 16	$s3=Mem[$sp+16]
Data Transfer	Store word	sw	I	0111	sw / $s3,16	Mem[$sp+16]=$s3
Data Transfer	Display	dsp	I	1000	dsp	Display the value of $out
Data Transfer	Input	inp	I	1001	inp $s3	$in will get a data and pass it to $s3
Data Transfer	Output	otp	I	1010	otp $s2	Load $out with $s2 and show
Conditional	Check equality	beq	I	1011	Beq / $s3,7	If($s3==$sp) then 7
Conditional	Compare less than	slt	R	1100	slt / $s1,$s2	If($s1<$s2)then / $sp=1 / else $sp=0
Unconditional	Jump	jmp	I	1101	jmp 12	Go to line 12

Formats:
We would like to use two types of formats for our ISA. They are:
- Register Type – R type
- Immediate Type – I type

R Type ISA Format:

Opcode	rd	rs
4 bits	4 bits	4 bits

I Type ISA Format:

Opcode	rd	Immediate
4 bits	4 bits	4 bits

List of Register:
As we have allocated four bits register so the number of register will be 24 = 16.
For input and output purpose we included 2 register $in and $out. But we didn’t added them here as they can not be accessed by the the users.
Register Number	Conventional Name	Usage	Binary Value
0	$sp	Storing value	0000
1	$s1	General purpose	0001
2	$s2	General purpose	0010
3	$s3	General purpose	0011
4	$s4	General purpose	0100
5	$s5	General purpose	0101
6	$s6	General purpose	0110
7	$s7	General purpose	0111
8	$s8	General purpose	1000
9	$s9	General purpose	1001
10	$s10	General purpose	1010
11	$s11	General purpose	1011
12	$s12	General purpose	1100
13	$s13	General purpose	1101
14	$s14	General purpose	1110
15	$s15	General purpose	1111

Translating Some HLL codes using our Designed 12 Bit ISA

      - a = a + b	#$s1 = a, $s2 = b
add $s1, $s2	# $s1 gets $s1 + s2

      - a = a – b	#$s1 = a, $s2 = b
sub $s1, $s2	# $s1 gets $s1 - s2

      - a = a AND b	#$s1 = a, $s2 = b
And $s1, $s2	# $s1 gets $s1 && $s2

      - 4. a = Not(a)	#$s1 = a
Nand $s1, $s1	# $s1 gets inverted value of $s1

      - C = A[i]	#$s1 = I, $s2=A , $s3=C
sll $s1, 2	# $sp = $s1<< 2
add $s2 $sp	#$s2 = $s2 + $sp
lsp $s2	# $sp = $s2
lw s3 0	# getting the location value of A[i] from sp and store
# them in s3.

6. if(i ==4)
i = i+2
else
i = i -2	# $s1 = i

sub $sp, $sp	# $sp = 0
addi $sp, 4	# $sp = 4
beq $s1 L	#comparing $s1 = i with $sp = 4. If equal then go to L
addi $s1, -2	# i = i – 2
jmp exit	# Jump to exit
L: addi $s1, 2	# i = i + 2

7. for(int j = 3; j < a; j++){
b = b*8;
}	# $s1 = j, $s2 = a, $s3 = b
sub $s1, $s1	# $s1 = 0
addi $s1, 3	# initializing $s1 = 3
sub $sp, $sp	# $sp = 0
add $sp, $s2	# $sp = $s2
L2: beq $s1 L1	#if $s1 = sp then go to L1, otherwise continue loop.
sll $s3 3	# $sp = $s3 << 3
add $s3 $sp	# $s3 = $s3 * 8
addi $s1 1	# increment $s1 by 1 / i++
jmp L2	# go to the loop
L1: exit.

Limitations:
- As we have only 12-bit that’s why we have to declare only 2 operands instead of 3 operands.
- We have divided our 12-bit in 3 divisions. That’s why we couldn’t reserve space for shift amount. Thus we used the immediate 4-bit space in I type format for shifting purpose.